QE-2021: Hands-on session – Day-4
Advanced functionals
Iurii Timrov (EPFL, Switzerland)

---
Outline
Exercise 1: DFT+U study of FeO
Exercise 2: DFT with hybrid functionals: study of Si
Exercise 3: DFT with Van der Waals functionals: study of graphite

---
Outline
Exercise 1: DFT+U study of FeO
Exercise 2: DFT with hybrid functionals: study of Si
Exercise 3: DFT with Van der Waals functionals: study of graphite

---
DFT+U
The DFT+U total energy:
The Hubbard correction energy:
effective Hubbard
      parameter
The occupation matrix:
The total occupation of localized states (d or f) at site I :
The Kohn-Sham equation:

---
Localized-states manifold
How do we know to what states of a Hubbard atom the Ueff correction will be applied?
Currently, this is hard-coded (in Quantum ESPRESSO 6.7)
Check two subroutines in quantum-espresso/Modules :
set_hubbard_n.f90
set_hubbard_l.f90
principal quantum number “n”
orbital quantum number “l”
For Fe : n = 3
For Fe : l = 2
Apply the Hubbard Ueff correction to the 3d electrons of Fe

---
Input file pw.FeO.scf.in
SCF calculation
Experimental lattice parameter
'MV' smearing for metals (FeO is metallic @PBEsol)
Spin-polarized (collinear) calculation
(antiferromagnetic ordering)
Initialize Hubbard parameters for two types of Fe
Two sublattices of Fe atoms
O
Fe

---
Input file pw.FeO.nscf.in
NSCF calculation
NSCF input is very similar to the SCF input,
 but there are a few differences which are
        highlighted here
Number of electronic bands
Projected DOS must be converged with respect to
the number of k points. Also, number of bands must
be large enough, to have converged projected DOS
in a specific energy range. All this is controlled here.
k points mesh which is denser than in SCF

---
Input file projwfc.FeO.in
Simple Gaussian broadening of PDOS
Value of Gaussian broadening, in Ry (not eV!)
Minimum and maximum value of energy for the plot, in eV
Energy grid step
Gnuplot script: plot_pdos.gp
Inspect the script: it aims at plotting Fe-3d state (majority spin and minority spin)
and O-2p states.
PDOS is shifted such that the Fermi energy corresponds to the zero of energy.
Visualize the file “FeO_PDOS.eps”

---
PDOS of FeO from standard DFT calculation
DFT predicts FeO to be metallic (but this is wrong!)
Let's try DFT+U
Experimentally FeO is know to be insulating

---
Input file pw.FeO.scf.in for DFT+U
Here we want to put a Hubbard U correction for
        3d electrons of Fe atoms
Which value of U to use?
For every material Hubbard U is different; here we use
U = 4.6 eV for Fe-3d states (see next slides)
Hubbard U values (in eV) for atomic type 1 & type 2

---
DFT vs DFT+U
DFT+U
DFT
The solution with DFT+U is insulating
The solution with DFT+U is metallic
Agreement with the experiement!

---
How to compute the Hubbard U parameter?
Linear response theory
Density-functional perturbation theory (DFPT)
Sum over all q points in a q mesh

---
How to compute the Hubbard U parameter?
Using the HP (Hubbard Parameters) code of Quantum ESPRESSO
Input file “hp.FeO.in”:
Prefix and outdir must be exactly the same as in
the input file LiCoO2.pw.in
Size of the q point mesh: 1x1x1 in this case
U = 4.6 eV
Warning: This U value is not converged with respect to the k and q meshes!!!
Documentation: quantum-espresso/HP/Doc/INPUT_HP.txt
Theory:
I. Timrov, N. Marzari, M. Cococcioni, PRB 98, 085127 (2018)
I. Timrov, N. Marzari, M. Cococcioni, PRB 103, 045141 (2021)

---
DFT+U+V
Both U and V can be
computed using the
HP code
V.L. Campo Jr and M. Cococcioni, JPCM 22, 055602 (2010)
Theory:
I. Timrov, N. Marzari, M. Cococcioni, PRB 103, 045141 (2021)

---
Outline
Exercise 1: DFT+U study of FeO
Exercise 2: DFT with hybrid functionals: study of Si
Exercise 3: DFT with Van der Waals functionals: study of graphite

---
We need to setup the q mesh

---
Input file pw.Si.scf.in
Hybrid functionals are very computationally expensive!
SCF calculation
Override the functional written in the pseudo-
potential (PP) file.
Important: use a PP for the closest GGA (PBE
in this case), there are no PP's for hybrids.
Mesh for the q points 1x1x1 is the minimal
grid (q=0), it is fast but not very accurate
If .true. use extrapolation for the q->0 limit
Specifies that the singularity at q->0 is
analytically integrated

---
Popular hybrid functionals
input_dft = “pbe0”
J.P.Perdew, M. Ernzerhof, K.Burke, JCP 105, 9982 (1996)
C. Adamo, V. Barone, JCP 110, 6158 (1999)
input_dft = “b3lyp”
 P.J. Stephens,F.J. Devlin,C.F. Chabalowski,M.J. Frisch, J.Phys.Chem 98, 11623 (1994)
input_dft = “hse”
Heyd, Scuseria, Ernzerhof, J. Chem. Phys. 118, 8207 (2003)
Heyd, Scuseria, Ernzerhof, J. Chem. Phys. 124, 219906 (2006)

---
Types of treatement of divergences at q->0

---
Convergence of the total energy
wrt q point grid
Slow calculations do for scarce q meshes and check the “reference” folder

---
Outline
Exercise 1: DFT+U study of FeO
Exercise 2: DFT with hybrid functionals: study of Si
Exercise 3: DFT with Van der Waals functionals: study of graphite

---
Graphite
Graphite has Van der Waals (dispersive) interactions between layers.
The equilibrium inter-layer distance is too small with LDA, and too large with GGA
        with respect to the experimental value (3.336 A).
Van der Waals interactions must be taken into account.

---
Input file pw.graphite.vc-relax.in
Variable-cell optimization
Variable-cell optimization
Hexagonal lattice, a and c are in Angtrom!
Override the functional written in the PP file.
Important: use PP for the closest GGA (PBE in
this case), because there are no PP for non-
local functionals
If we do not specify anything inside these namelists,
then the default values will be used for various
control parameters
The k point grid is denser along xy than along z,
reflecting shorter periodicity in the xy plane

---
Types of the van der Waals correction

---
Structural optimization in graphite