QE-2021: Hands-on session – Day-6
TDDFPT
Iurii Timrov (EPFL, Switzerland)
Oscar Baseggio (SISSA, Italy)

---
Outline
1. Exercise 1: Calculation of absorption spectra in the Independent Particle Approximation
2. Exercise 2: Calculation of absorption spectra of interacting electrons using the turboDavidson program
3. Exercise 3: Calculation of absorption spectra of interacting electrons using the turboLanczos program
4. Exercise 4: Convergence of absorption spectra of Na2

---
Outline
1. Exercise 1: Calculation of absorption spectra in the Independent Particle Approximation
2. Exercise 2: Calculation of absorption spectra of interacting electrons using the turboDavidson program
3. Exercise 3: Calculation of absorption spectra of interacting electrons using the turboLanczos program
4. Exercise 4: Convergence of absorption spectra of Na2

---
Independent Particle Approximation
The simplest approximation: Independent Particle Approximation (IPA) which allows us to describe single-particle excitations.
Fermi's golden rule
The transition probability per unit time from occupied states to empty states reads:
is the external potential induced by the electric field.
and
are the eigenvalues
are the eigenvalues
and the eigenfunctions of the ground-state Kohn-Sham equation
Absorption coefficient:

---
Exercise 1: Calculation of absorption spectra in IPA
Go to the directory with the input files:
cd Hands-on_TDDFPT_ABS/exercise1
In this directory you will find:
- README – File describing how to do the exercise
- Benzene.scf.in – Input file for the SCF ground-state calculation
- Benzene.epsilon.in – Input file for a calculation of spectrum in IPA
- H.vbc.UPF – Pseudopotential of hydrogen
- C.vbc.UPF – Pseudopotential of carbon
- plot_spectrum.gnu – Script to plot spectrum using gnuplot
- reference – Directory with the reference results
- out – Directory for temporary files

---
Exercise 1: Calculation of absorption spectra in IPA
Step 1. Perform a Self-Consistent Field ground-state calculation for benzene at the equilibrium structure using the pw.x program.
Benzene.scf.in
pw.x < Benzene.scf.in > Benzene.scf.out
Output
Input

---
Exercise 1: Calculation of absorption spectra in IPA
The output SCF file Benzene.scf.out :
HOMO
LUMO
HOMO – Highest Occupied Molecular Orbital
LUMO – Lowest Unoccupied Molecular Orbital
Energy gap = LUMO – HOMO = 5.1 (eV)

---
Exercise 1: Calculation of absorption spectra in IPA
Step 2. Perform a calculation of the absorption spectrum of benzene in the Independent Particle Approximation using the epsilon.x program.
Benzene.epsilon.in
Input file for the calculation of spectrum
epsilon.x < Benzene.epsilon.in > Benzene.epsilon.out

---
Exercise 1: Calculation of absorption spectra in IPA
The code epsilon.x produces 4 files:
- epsr.dat – Real part of the response
- epsi.dat – Imaginary part of the response (this is what we need)
- eels.dat – Electron energy loss spectrum
- ieps.dat – Response computed on the imaginary axis of frequency
  The content of epsi.dat looks like:
Use gnuplot and the script plot_spectrum.gnu in order to plot the absorption spectrum of benzene Benzene_spectrum.eps

---
Exercise 1: Calculation of absorption spectra in IPA
Absorption spectrum of benzene in the Independent Particle Approximation (file Benzene_spectrum.eps):
Energy gap = LUMO – HOMO = 5.1 (eV)

---
Outline
1. Exercise 1: Calculation of absorption spectra in the Independent Particle Approximation
2. Exercise 2: Calculation of absorption spectra of interacting electrons using the turboDavidson program
3. Exercise 3: Calculation of absorption spectra of interacting electrons using the turboLanczos program
4. Exercise 4: Convergence of absorption spectra of Na2

---
turboDavidson program for calculations of absorption spectra
- The turbo_davidson.x program allows us to calculate absorption spectra of molecules using time-dependent density functional perturbation theory (TDDFpT).
- The interactions of electrons (Hartree and Exchange-Correlation effects) are taken into account fully ab initio and self-consistently.
- The electronic transitions from occupied to empty states can be analyzed by selecting a frequency range in which the transitions occur.
- However, calculations of overall absorption spectra in a wide frequency range are computationally rather expensive, because many eigenvalues of the Hamiltonian must be computed.
Theory: Xiaochuan Ge, PhD thesis “Seeing colors with TDDFT”, SISSA (2013).

---
turboDavidson program for calculations of absorption spectra
Coupled linear-response TDDFpT equations (resonant and anti-resonant):
These equations can be re-written as Casida's matrix equation:
interaction terms
where and
Davidson algorithm is used (the same algorithm as in the ground state SCF calculation) to solve the Casida's equations and to obtain the eigenvalues which are used for a calculation of the absorption coefficient.

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Go to the directory with the input files:
cd Hands-on_TDDFPT_ABS/exercise2
In this directory you will find:
- README – File describing how to do the exercise
- Benzene.scf.in – Input file for the SCF ground-state calculation
- Benzene.davidson.in – Input file for a Davidson calculation of the eigenvalues
- Benzene.tddfpt_pp.in – Input file for a post-processing calculation of the spectrum
- H.vbc.UPF – Pseudopotential of hydrogen
- C.vbc.UPF – Pseudopotential of carbon
- plot_spectrum.gnu – Script to plot spectrum using gnuplot
- reference – Directory with the reference results
- out – Directory for temporary files

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Step 1. Perform a SCF ground-state calculation:
pw.x < Benzene.scf.in > Benzene.scf.out
Step 2. Perform the turboDavidson calculation without the electronic interaction using the turbo_davidson.x program.
turbo_davidson.x < Benzene.davidson.in > Benzene.davidson.out

---
Exercise 2: Calculation of absorption spectra using turboDavidson
The code turbo_davidson.x produces a file Benzene-dft.eigen containing single-particle excitation eigenvalues:

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Step 3. Perform a spectrum calculation using the turbo_spectrum.x program and using the eigenvalues computed in the previous step.
The input file Benzene.tddfpt_pp.in reads:
turbo_spectrum.x < Benzene.tddfpt_pp.in > Benzene.tddfpt_pp.out

---
Exercise 2: Calculation of absorption spectra using turboDavidson
The turbo_spectrum.x program produces the file Benzene.plot which contains the absorption spectrum in a tabular format:

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Step 4. Plot the spectrum using gnuplot and the script plot_spectrum.gnu
Since the interaction was switched off (if_dft_spectrum=.true.), you should obtain the same absorption spectrum as the one obtained using the epsilon.x program in the exercise1.
The script plot_spectrum.gnu will do such a comparison, and it will produce the file Benzene_spectrum.eps which you can visualize.

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Comparison of the absorption spectrum of benzene computed in the Independent Particle Approximation using turbo_davidson.x and epsilon.x (file Benzene_spectrum.eps):

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Now switch on the interaction!
Make the following modifications in the input files:
- In the file Benzene.davidson.in set if_dft_spectrum = .false.
- In the file Benzene.tddfpt_pp.in set eign_file = 'Benzene.eigen'
- In plot_spectrum.gnu change the title to: 'turbo-davidson.x (interacting electrons)'
  Once these modifications are done, repeat steps 2, 3, and 4:
Note! The calculation will be a bit too long: 15 minutes using 2 cores. Therefore, let us see the output files in the directory 'reference'.

---
Exercise 2: Calculation of absorption spectra using turboDavidson
Comparison of the absorption spectrum of benzene computed using turbo_davidson.x with interaction and using epsilon.x in the Independent Particle Approximation (file Benzene_spectrum.eps):
Interaction opens the gap and blue-shifts the peaks

---
Outline
1. Exercise 1: Calculation of absorption spectra in the Independent Particle Approximation
2. Exercise 2: Calculation of absorption spectra of interacting electrons using the turboDavidson program
3. Exercise 3: Calculation of absorption spectra of interacting electrons using the turboLanczos program
4. Exercise 4: Convergence of absorption spectra of Na2

---
turboLanczos program for calculation of absorption spectra
- The turbo_lanczos.x program allows us to calculate absorption spectra of molecules using time-dependent density functional perturbation theory (TDDFpT) without computing empty states!
- The interactions of electrons (Hartree and Exchange-Correlation effects) are taken into account fully ab initio and self-consistently.
- The electronic transitions from occupied to empty states cannot be analyzed (use turbo_davidson.x for this purpose).
- The overall absorption spectrum in a wide frequency range can be calculated at once!
Theory: Dario Rocca, PhD thesis “TDDFT: New algorithms with applications to molecular spectra”, SISSA (2007).

---
turboLanczos program for calculation of absorption spectra
Coupled linear-response TDDFpT equations (resonant and anti-resonant):
perturbation
interaction terms
These equations can be re-written as a quantum Liouville equation:
Absorption coefficient is computed as:
Lanczos algorithm is used to solve recursively quantum Liouville equation in the standard batch representation. This allows us to avoid inversions and multiplications of large matrices.

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Go to the directory with the input files:
cd Hands-on_TDDFPT_ABS/exercise3
In this directory you will find:
- README – File describing how to do the exercise
- Benzene.scf.in – Input file for the SCF ground-state calculation
- Benzene.lanczos.in – Input file to perform Lanczos recursions
- Benzene.tddfpt_pp.in – Input file for a postprocessing calculation of spectrum
- H.vbc.UPF – Pseudopotential of hydrogen
- C.vbc.UPF – Pseudopotential of carbon
- plot_spectrum.gnu – Script to plot spectrum using gnuplot
- reference – Directory with the reference results
- out – Directory for temporary files

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Step 1. Perform a SCF ground-state calculation:
pw.x < Benzene.scf.in > Benzene.scf.out
Step 2. Perform Lanczos recursions using the turbo_lanczos.x program The input file is Benzene.lanczos.in :
turbo_lanczos.x < Benzene.lanczos.in > Benzene.lanczos.out

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Note! The calculation will be a bit too long: 35 minutes using 2 cores. Therefore, let us see the output files in the directory reference.
In the output file Benzene.lanczos.out there is information about each Lanczos iteration :
In the directory out, which contains temporary files, there is a file Benzene.beta_gamma_z.1 which contains the information about Lanczos coefficients:

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Step 3. Perform a spectrum calculation using the post-processing program turbo_spectrum.x and using the Lanczos coefficients computed in the previous step.
The input file Benzene.tddfpt_pp.in reads:
turbo_spectrum.x < Benzene.tddfpt_pp.in > Benzene.tddfpt_pp.out

---
Exercise 3: Calculation of absorption spectra using turboLanczos
The code turbo_spectrum.x produces a file Benzene.plot_chi.dat which can be used for plotting the absorption spectrum :

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Step 4. Plot the spectrum using gnuplot and the script plot_spectrum.gnu
You should obtain the same excitation peak in the spectrum as was obtained using the code turbo_davidson.x in the exercise2 including interaction.
The script plot_spectrum.gnu will do such a comparison, and it will produce the file Benzene_spectrum.eps which you can visualize.

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Comparison of the absorption spectrum of benzene computed using turbo_lanczos.x and using turbo_davidson.x both including the interation (file Benzene_spectrum.eps):

---
Exercise 3: Calculation of absorption spectra using turboLanczos
turbo_lanczos.x allows us to obtain the absorption spectrum in a wide frequency range just by repeating a post-processing calculation using turbo_spectrum.x in a larger frequency range. This cannot be done with turbo_davidson.x
Make changes in Benzene.tddfpt_pp.in
turbo_spectrum.x < Benzene.tddfpt_pp.in > Benzene.tddfpt_pp.out

---
Exercise 3: Calculation of absorption spectra using turboLanczos
turbo_lanczos.x allows us to obtain the absorption spectrum in a wide frequency range just by repeating a post-processing calculation using turbo_spectrum.x in a larger frequency range. This cannot be done with turbo_davidson.x
Make changes in the script plot_spectrum.gnu:
set xrange [0:30.0]
set xlabel 0.0, 5.0, 30.0
Use gnuplot and the modified script plot_spectrum.gnu to produce the graph Benzene_spectrum.eps .

---
Exercise 3: Calculation of absorption spectra using turboLanczos
Comparison of the absorption spectrum of benzene computed using turbo_lanczos.x and using turbo_davidson.x both including the interation (file Benzene_spectrum.eps):
Many more eigenvalues must be computed in turboDavidson in order to obtain spectrum in a wide frequency range!
One Lanczos calculation to obtain spectrum in any wide frequency range!

---
Comparison of the absorption spectra of
benzene and naphthalene
In naphthalene the pi-orbitals are more delocalized than in benzene, which leads to smaller energy gap, and which hence red-shifts the peaks.

---
Comparison of the absorption spectra of benzene
using local and non-local XC functionals
Hybrid exchange-correlation functionals open the energy gap and blue-shift the peaks (SCF: input_dft='PBE0', Lanczos: d0psi_rs=.true.)

---
Outline
1. Exercise 1: Calculation of absorption spectra in the Independent Particle Approximation
2. Exercise 2: Calculation of absorption spectra of interacting electrons using the turboDavidson program
3. Exercise 3: Calculation of absorption spectra of interacting electrons using the turboLanczos program
4. Exercise 4: Convergence of absorption spectra of Na2

---
Exercise 4: Convergence of absorption spectra of Na2
Go to the directory with the input files:
cd Hands-on_TDDFPT_ABS/exercise4
Study the convergence of the absorption spectrum of Na2 with respect to:
- The number of Lanczos iterations itermax = 50, 100, 150,... without using the extrapolation extrapolation = 'no'
- How many Lanczos iterations is needed to converge the spectrum when the extrapolation is used extrapolation = 'osc'?
- The size of the supercell celldm(1) = 20, 30, 40, ...

---
Exercise 4: Convergence of absorption spectra of Na2
No extrapolation of Lanczos coefficients
Na.lanczos.in
Na.tddfpt_pp.in
Must be equal !
You can use restart = .true. option in order not to start from scratch, when you want to increase the number of Lanczos iterations.

---
Exercise 4: Convergence of absorption spectra of Na2
No extrapolation of Lanczos coefficients

---
Exercise 4: Convergence of absorption spectra of Na2
Behaviour of Lanczos coefficients
Lanczos coefficients oscillate around half of the kinetic-energy cutoff (50/2 = 25 Ry in this case). Hence, we can extrapolate these coefficients.

---
Exercise 4: Convergence of absorption spectra of Na2
Extrapolation of Lanczos coefficients
In the Liuoville-Lanczos approach, the absorption coefficient is computed as:
where is the tridiagonal matrix composed of the Lanczos coefficients.
Extrapolation

---
Exercise 4: Convergence of absorption spectra of Na2
Extrapolation of Lanczos coefficients
Na.lanczos.in
Na.tddfpt_pp.in
Must be equal !
Number up to which we extrapolate (can be very large at negligible cost)
The extrapolation technique can be used if the number of Lanczos coefficients is larger than 150 (internal threshold in the turbo_spectrum.x program).

---
Exercise 4: Convergence of absorption spectra of Na2
Extrapolation of Lanczos coefficients
The convergence of the absorption spectrum is reached (much) faster if the extrapolation technique is used (especially for large systems)!

---
Exercise 4: Convergence of absorption spectra of Na2
Convergence with respect to the size of the supercell

---
Outline
1. Introduction
2. Exercise 1: Calculation of EELS of bulk silicon
3. Exercise 2: Convergence of EELS of bulk silicon
4. Exercise 3: Calculation of EELS of Al(111)

---
Outline
1. Introduction
2. Exercise 1: Calculation of EELS of bulk silicon
3. Exercise 2: Convergence of EELS of bulk silicon
4. Exercise 3: Calculation of EELS of Al(111)

---
Basic equations
Coupled (resonant and anti-resonant) frequency-dependent Kohn-Sham equations:
perturbation
interaction terms
These equations can be re-written as a quantum Liouville equation:
Susceptibility
Loss function

---
Outline
1. Introduction
2. Exercise 1: Calculation of EELS of bulk silicon
3. Exercise 2: Convergence of EELS of bulk silicon
4. Exercise 3: Calculation of EELS of Al(111)

---
Exercise 1: Calculation of EELS of bulk silicon
Go to the directory with the input files:
cd Hands-on_TDDFPT_EELS/exercise1
In this directory you will find:
- README – File describing how to do the exercise
- Si.scf.in – Input file for the SCF ground-state calculation
- Si.eels.in – Input file for a Lanczos calculation
- Si.tddfpt_pp.in – Input file for a spectrum calculation
- Si.pz-vbc.UPF – Pseudopotential of silicon
- plot_spectrum.gnu – Script to plot spectrum using gnuplot
- reference – Directory with the reference results
- out – Directory for temporary files

---
Exercise 1: Calculation of EELS of bulk silicon
Step 1. Perform a Self-Consistent Field ground-state calculation for silicon at the equilibrium structure using the pw.x program.
Si.scf.in
pw.x < Si.scf.in > Si.scf.out
Input
Output

---
Exercise 1: Calculation of EELS of bulk silicon
Step 2. Perform Lanczos recursions using the turbo_eels.x program in order to compute Lanczos coefficients, which will be needed in Step 3.
Si.eels.in
How to specify q1, q2, q3 ? -> Next slide
turbo_eels.x < Si.eels.in > Si.eels.out

---
Exercise 1: Calculation of EELS of bulk silicon
Step 2. Perform Lanczos recursions using the turbo_eels.x program in order to compute Lanczos coefficients, which will be needed in Step 3.
- lattice parameter
Example: and .
Therefore, we obtain:

---
Exercise 1: Calculation of EELS of bulk silicon
In the output file Si.eels.out there is information about each Lanczos iteration :

---
Exercise 1: Calculation of EELS of bulk silicon
Step 3. Perform a spectrum calculation using the post-processing program turbo_spectrum.x and using the Lanczos coefficients computed in the previous step.
Si.tddfpt_pp.in
turbo_spectrum.x < Si.tddfpt_pp.in > Si.tddfpt_pp.out

---
Exercise 1: Calculation of EELS of bulk silicon
The code turbo_spectrum.x produces a file Si.plot_chi.dat which contains the real and imaginary parts of the polarizability :

---
Exercise 1: Calculation of EELS of bulk silicon
The code turbo_spectrum.x also produces a file Si.plot_eps.dat which contains the real and imaginary parts of the dielectric function and its inverse:

---
Exercise 1: Calculation of EELS of bulk silicon
The code turbo_spectrum.x also produces a file Si.plot_eps.dat which contains the real and imaginary parts of the dielectric function and its inverse:

---
Exercise 1: Calculation of EELS of bulk silicon
Step 4. Plot the spectrum using gnuplot and the script plot_spectrum.gnu
Electron Energy Loss Spectrum of bulk silicon (file Spectrum.eps):
Is the spectrum converged? -> exercise2 What is the origin of peaks?

---
Exercise 1: Calculation of EELS of bulk silicon
The code turbo_spectrum.x also produces a file Si.plot_eps.dat which contains the real and imaginary parts of the dielectric function and its inverse:

---
Exercise 1: Calculation of EELS of bulk silicon
What is the origin of peaks?
plasmon

---
Outline
1. Introduction
2. Exercise 1: Calculation of EELS of bulk silicon
3. Exercise 2: Convergence of EELS of bulk silicon
4. Exercise 3: Calculation of EELS of Al(111)

---
Exercise 2: Convergence of EELS of bulk silicon
Go to the directory with the input files:
cd Hands-on_TDDFPT_EELS/exercise2
1. Study the convergence of the loss spectrum of bulk silicon with respect to:
- k points mesh
- Number of Lanczos iterations
  2. Compute the plasmon dispersion, i.e. change in the position of the plasmon peak when changing the value of the transferred momentum:

---
Exercise 2: Convergence of EELS of bulk silicon
Convergence of EELS with respect to the k points mesh
Here, 400 Lanczos iterations + extrapolation was used.

---
Exercise 2: Convergence of EELS of bulk silicon
Convergence of EELS with respect to the number of Lanczos iterations (no extrapolation)
Here, k points mesh 10x10x10 1 1 1 was used.

---
Exercise 2: Convergence of EELS of bulk silicon
Convergence of EELS with respect to the number of Lanczos iterations (with and without extrapolation)
Here, k points mesh 10x10x10 1 1 1 was used.

---
Exercise 2: Convergence of EELS of bulk silicon
Plasmon dispersion in bulk silicon
Here, k points mesh 10x10x10 1 1 1 was used and 400+extrapol. Lanczos iterations. By incresing q, the plasmon peak blue-shifts and broadens, because it enters in the electron-hole continuum.

---
Exercise 2: Convergence of EELS of bulk silicon
The excitation region of the electron gas in (q,w) space
The plasmon line becomes higly damped in the region of electron-hole pairs, which is shown hatched.
G. D. Mahan, Many-Particle Physics, Plenum Press, 2nd ed. New York, (1975)